## Slide 1
Dr. Uttam Ghosh
Computer Science
Vanderbilt University
Uttam.ghosh@vanderbilt.edu
An Overview of Software Defined Networking (SDN)

## Slide 2: The Present Era….

## Slide 3: OS Support for Networking- Where are We?
Operating System
Network Interface Card
Kernel Space
Hardware
User Space
Application
Application
Application
Network
Physical Layer
Ethernet Driver
Application Layer
Transport Layer
Network Layer
Data Link Layer
TCP
HTTP
IP
Ethernet

## Slide 4: Interaction between Layers in TCP/IP Stack
Physical Layer
Data Link Layer
Physical Layer
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Application Layer
Transport Layer
Network Layer
Data Link Layer
Host 1
Forwarding device (Switch)’
Host 2
Layer 5
Layer 4
Layer3
Layer 2
Layer 1
Physical Communication
Interface
Protocol

## Slide 5: Goal of the Lecture
We will discuss the traditional networking and how Software Defined Networking brings the revolution using network operating system (NOS).
Software Defined Networking – the biggest break through of computing of the last decade.
We will categorically elaborate the features which make SDN an emerging technology.
Finally we will discuss SDN integration- applications of SDN.
Notes: SDN separates the control plane from the data plane freeing software innovation cycles to become independent of hardware innovation cycles.
SDN accelerates Internet and Cloud innovation while significantly reducing the costs of building and operating networks.
A PhD dissertation of Martin Casado, Stanford [2008]

## Slide 6: Planes of Network
Data Plane:
  Data forwarding and processing.
  Runs at line rate (Fast Path).
Control Plane:
  Make forwarding decisions (routing table) and program (packet handling policies) data plane
  Handled by CPU
Management Plane:
  Responsible for controlling and monitoring of network devices
  Instantiate new devices and protocols (turn devices on/off)
Switch
Data Plane
Control Plane
CPU
Memory
Forwarding Hardware

## Slide 7: Problem of Legacy Network Devices
Too Complicated:
Control plane is implemented with complicated software and hardware
Closed Platform: Vendor Specific
Hard to Modify (nearly impossible):
Hard to add new functionalities (applications)
New proposal: Software Defined Networking
Specialized Data
Forwarding H/W
Operating System
App
App
App
…
Specialized Data
Forwarding H/W
Operating System
App
App
App
…
Specialized Data
Forwarding H/W
Operating System
App
App
App
…
Specialized Data
Forwarding H/W
Operating System
App
App
App
…
Closed
Cannot dynamically change according to network conditions
Notes: Control plane is implemented with complicated software (million of lines of source code) and hardware (billion of gates)

## Slide 8: Legacy Network Versus SDN
Data Plane
Control Plane
Data Plane
Control Plan
Data Plane
Control Plane
Data Plane
Control Plane
Control Agent
Data Plane
SDN Control Plane
SDN Application
SDN Application
SDN Application
SDN Application
Control Agent
Data Plane
Control Agent
Data Plane
Software Defined Network
Separation of control plane and data plane
Open interface between control plane and data plane
Easy to add new functionalities (applications) as control plane is programmable
Legacy/Traditional Network
Network of closed and proprietary components (switches)
Legacy Network
Software Defined Network

## Slide 9: Key Idea: Separation of Control & Data Planes
Switches only have forwarding elements.
OpenFlow is the protocol to send/receive forwarding rules from controller to switches.
OpenFlow should be reliable (TCP) and secure (SSL).
Control Plane Intelligence
Secure Channel
Flow Table
Secure Channel
Flow Table
Secure Channel
Flow Table
OpenFlow Protocol
OpenFlow (OF) Switch
OpenFlow (OF) Switch
OpenFlow (OF) Switch
Controller
OpenFlow switch
Secure and reliable channels
Control logic is moved to a controller.
One controller (mostly Open Source) with a lot of cheap switches.

## Slide 10: SDN Architecture
Network Infrastructure
North Bound Interface
Forwarding Devices
SDN Applications
Routing
QoS
Management
Application Plane
Data Plane
Network Operating System(SDN Controller)
Control
Plane
Global View
South Bound Interface

## Slide 11: What is SDN?
The physical separation of the network control plane from the forwarding (data) plane, and where a control plane controls several devices.
Directly programmable: Controller is programmable.
Agile: Abstracting control from forwarding
Centrally managed: Controller is logically centralized.
Programmatically configured: Network can be configured by controller programs.
Open standards-based vendor neutral

## Slide 12: OpenFlow: Bootstrapping
Switches need initial configuration: Switch IP address, controller IP address and default gateway
Switches connect to the controller
Controller sends a LLDP request to all neighbors (switches)
Switch
Controller
Switch provides configuration information about ports
Controller determines the topology from LLDP responses

## Slide 13: SDN: Working Principles
Network Operating System
Topology Manager
Routing Manager
Host Tracker
Switch Manager
SDN Controller
Control Plane
Data Plane
S1
S2
S3
S4
H2
H2 sends packet to S3
S3 forwards the packet to Controller
Controller computes path S3-S2-S1 and sends flow rules to switches:
For S3: H2 S2: Forward
For S2: S3 S1: Forward
For S1: S2 H1: Forward
1
1
2
2
3
3
3
3
S3, S2 and S1 forward the packet to H1 as per flow table.
4
4
4
H1
4
H2 sends remaining packets to
H1 through S3-S2-S1 as a flow.
H2-S3-S2-S1-H2
5
5

## Slide 14: Virtualization using SDN
Controller
Switch
Host 1
Host 2
Host 3
Switch
Host 4
Host 5
Host 6
VLAN 0
VLAN 1
VLAN 2
VLAN Manager
App Manager-
Switch

## Slide 15: Dynamic Slicing
Slicing software like FlowVisor slices OpenFlow networks, creating multiple isolated and programmable logical networks on the same physical topology.
Tenants need complete control over their addresses, topology, and routing, security. SDN provides virtual tenant network using dynamic slicing from a same physical substrate.
Virtual Network 2
Virtual Network 1
Physical Network

## Slide 16: Service Integration in SDN
Network Operating System
Firewall
Routing Manager
Host Tracker
Topology Manager
SDN Controller
Control Plane
Data Plane
S1
S2
S3
S4
H2
Firewall.c
.. .
If (pkt->tcp->dport == 80)
dropPacket(pkt);
.. .
H1
Load balancers, firewalls, Intrusion Detection Systems (IDS), provisioned on demand and placed appropriately on the traffic path

## Slide 17: Integration of SDN: Applications
Cloud Computing
Internet of Things
Mobile Computing
Information Centric Networking (ICN)
Critical Infrastructure (Cyber Physical) Security

## Slide 18: Mininet- An Emulator for SDN
Mininet creates a realistic virtual network, running real kernel, switch and application code, on a single machine (VM, cloud or native), in seconds, with a single command.
Source: http://mininet.org/

## Slide 19: Forums and Standards
  ONF- Open Networking Foundation- open, collaborative consortium of industry academia
  How to reach: https://www.opennetworking.org/
  OpenDayLight – Linux Foundation Projects, open source SDN platform
  How to reach: https://www.opendaylight.org/
  ONOS - Open Network Operating System (ONOS) is an open source SDN network operating system designed for building next-generation SDN/NFV solutions.
  How to reach: https://onosproject.org/
  OpenStack: Open source software for creating private and public clouds.
  How to reach: https://www.openstack.org/
IEEE Standardization: IEEE standardization efforts to advance software defined networks are currently under way.
How to reach: https://sdn.ieee.org/standardization
IETF and RFC: Several ongoing proposals could be found in IETF and RFC.
How to reach: https://www.ietf.org/

## Slide 20: SDN Solution- State-of-the-art
Commercial H/W
OpenSource S/W
North Bound Interface
SDN Applications
Routing
QoS
Management
Application Plane
Data Plane
Control
Plane
South Bound Interface
HP
NEC
Cisco
Juniper
OpenVSwitch
Lagopus VSwitch
OpenWRT
ODL
RYU
NOX
POX
Floodlight
PFC
Source: https://www.sdxcentral.com/sdn/
RouteFlow
FlowVisor

## Slide 21: Recommended Reading
P. Saint-Andre, et al., “XMPP: The Definitive Guide,” O’Reilly, 2009, 320 pp., ISBN:9780596521264 (Safari Book)
Prof. Raj Jain, “Introduction to Software Defined Networking (SDN)”.
U. Ghosh, P. Chatterjee, S. Shetty, C. Kamhoua, and L. Njilla, “Towards Secure Software-defined Networking Integrated Cyber-Physical systems: Attacks and Countermeasures", in Springer Versatile Cyber-Security, 2019.
Kreutz et al., towards secure and dependable software-defined networks, SigCom 2013.
Shin et al., Attacking Software-Defined Networks: A First Feasibility Study , HotSDN, 2013.
U. Ghosh, Z. Wang, X. Dong, R. Tan, Z. Kalbarczyk, D. Yau and R. K. Iyer, “ An Empirical
Study on Smart Grid Resilience under Software-Defined Networking Controller Failures", in ACM CPSS 2016, Xi'an, China.