## Slide 1: An Introduction to Network Simulator (NS-2)
Dr. Uttam Ghosh
uttam.ghosh@vanderbilt.edu
Computer Science
Vanderbilt University
Network Simulation

## Slide 2: Outline
Introduction
Simulation- General Approach
Simulation- Wired
  Application Protocol: FTP, CBR
  Transport Protocol: UDP, TCP
  Routing Protocol: Static and Dynamic (DV)
Simulation- Mobile Ad Hoc Network (MANET)
  AODV, DSR, DSDV
Simulation- Hybrid (Wireless and Wired)

## Slide 3: What is NS?
Event Driven Simulator
  Physical activities are translated to events
  Events are queued and processed in the order of their scheduled occurrences
  Time progresses as the events are processed
Packet Level
1
2
Time: 1.5 sec
Time: 1.7 sec
Time: 1.8 sec
Time: 2.0 sec

## Slide 4: Simulation Support
Wired Networks
Wireless Networks
Satellite Networks
InterPlanetary Networks
Wireless Sensor Networks
Vehicular Ad hoc Networks
Mobile Ad hoc Networks

## Slide 5: Protocol Support
It supports all the layers of OSI
Collection of various protocols at multiple layers
  Application (FTP, WWW, CBR)
  TCP (reno, new reno, tahoe, vegas, sack)
  MAC(802.11, 802.3, TDMA)
Queuing model
Different mobility model in case of wireless networks
Ad-hoc routing (DSDV, DSR, AODV, TORA)
Sensor network (Diffusion, Gaf)
Multicast protocols, Satellite protocols, and many others

## Slide 6: NS Components
NS- Simulator
NAM- Network AniMator
Preprocessing (using C++)
Topology generator (using TCL)
Post analysis
Generates NAM (with .nam extension) and Trace (with .tr extension) files.
Trace analysis using Perl/TCL/AWK/MATLAB

## Slide 7: NS Environments
Simulation Scenario
Tcl Script
C++ Implementation
0
1
set ns [new Simulator]
set node_(0) [$ns node]
set node_(1) [$ns node]
class MobileNode : public Node
{
friend class PositionHandler;
public:
MobileNode();
•
•
}

## Slide 8: Network AniMator (NAM)

## Slide 9: Trace File (a.tr)
- 0.84824 2 3 tcp 1040 ------- 0 0.0 3.0 29 46
r 0.85408 2 3 tcp 1040 ------- 0 0.0 3.0 28 44
+ 0.85656 2 3 tcp 1040 ------- 0 0.0 3.0 30 47
- 0.85656 2 3 tcp 1040 ------- 0 0.0 3.0 30 47
r 0.8624 2 3 tcp 1040 ------- 0 0.0 3.0 29 46
+ 0.86488 2 3 tcp 1040 ------- 0 0.0 3.0 31 49
- 0.86488 2 3 tcp 1040 ------- 0 0.0 3.0 31 49
r 0.87072 2 3 tcp 1040 ------- 0 0.0 3.0 30 47
+ 0.8732 2 3 tcp 1040 ------- 0 0.0 3.0 32 50
- 0.8732 2 3 tcp 1040 ------- 0 0.0 3.0 32 50
r 0.87904 2 3 tcp 1040 ------- 0 0.0 3.0 31 49
+ 0.88152 2 3 tcp 1040 ------- 0 0.0 3.0 33 52
- 0.88152 2 3 tcp 1040 ------- 0 0.0 3.0 33 52
r 0.88736 2 3 tcp 1040 ------- 0 0.0 3.0 32 50

## Slide 10: NS Installation & Run
  Download: https://sourceforge.net/projects/nsnam/files/latest/download
  Unzip: $ tar -xzf ns-allinone-2.35.tar.gz
  Need to edit the line number 137 of ~/ns-allinone-2.35/ns-2.35/linkstate/ls.h:
  void eraseAll() { erase(baseMap::begin(), baseMap::end()); }
  to
  void eraseAll() { this->erase(baseMap::begin(),baseMap::end()); }
  Need gcc version 4.8: $sudo apt-get install gcc-4.8 g++-4.8
  Install allinone package: $export CC=gcc-4.8 CXX=g++-4.8 && ./install (run in ~/ns-allinone-2.35)
  *Validation: $./validate (run in ~/ns-allinone-2.35/ns-2.35/)
  *Configuration: $./configure ((run in ~/ns-allinone-2.35/ns-2.35/)
Notes: *Not Needed
** There will be no source code

## Slide 11: NS Installation & Run
  Set path (/etc/profile):
  PATH=$PATH:/home/uttam/ns-allinone-2.35/bin:/home/uttam/ns-allinone-2.35/tcl8.5.10/unix:/home/uttam/ns-allinone-2.35/tk8.5.10/unix:/home/uttam/ns-allinone-2.35/otcl-1.14:/home/uttam/ns-allinone-2.35/lib:/home/uttam/ns-allinone-2.35/tcl8.5.10/library
  Either restart or use: $source /etc/profile
  Automatic Installation: $sudo apt-get install ns2
  Verify your installation: $ns
    The output in the terminal should be %
  To Run Script (e.g., Simple.tcl): ns Simple.tcl
  To Run NAM (e.g., Simple.nam): nam Simple.nam

## Slide 12: Simulation- General Approach
Create the simulator
Activate tracing
Create the nodes and topology
Create the links
Activate routing
Chose error model, if necessary
Create the traffic
Send application data

## Slide 13: Wired Network- UDP
0
1
Agent/ UDP
Application/Traffic/CBR
Agent/ Null

## Slide 14: Simulator Creation and Tracing Activation
Creating a Simulator Object
  set ns [new Simulator]
Setting up files for trace & NAM
  set trace_nam [open out.nam w]
  set trace_all [open all.tr w]
Tracing files using their commands
  $ns namtrace-all $trace_nam
  $ns trace-all $trace_all
Closing trace file and starting NAM
  proc finish { } {
    global ns trace_nam trace_all
    $ns flush-trace
    close $trace_nam
    close $trace_all
    exec nam out.nam &
    exit 0 }

## Slide 15: Topology Creation
Creating two nodes
    set n0 [$ns node]
    set n1 [$ns node]
Creating links (topology) between two nodes
  $ns duplex-link $n0 $n1 1Mb 10ms DropTail

## Slide 16: Attaching Agents
Create a UDP agent and attach it to node n0
set udp0 [new Agent/UDP]
$ns attach-agent $n0 $udp0
Create a CBR traffic source and attach it to udp0
set cbr0 [new Application/Traffic/CBR]
$cbr0 set packetSize_ 500
$cbr0 set interval_ 0.005
$cbr0 attach-agent $udp0
Create a Null agent (a traffic sink) and attach it to node n1
set null0 [new Agent/Null]
$ns attach-agent $n1 $null0
Connect the traffic source with the traffic sink
$ns connect $udp0 $null0

## Slide 17: Traffic Generation
Schedule events for the CBR agent
$ns at 0.5 "$cbr0 start"
$ns at 4.5 "$cbr0 stop"
Call the finish procedure after 5 seconds of simulation time
$ns at 5.0 "finish"
Run the simulation
$ns run

## Slide 18: Wired Network- UDP
0
1
UDP/CBR packet

## Slide 19: Wired Network- TCP
0
1
Agent/ TCP
Application/FTP
Agent/ TCPSink

## Slide 20: Simulator Creation and Tracing Activation
Creating a Simulator Object
  set ns [new Simulator]
Setting up files for trace & NAM
  set trace_nam [open out.nam w]
  set trace_all [open all.tr w]
Tracing files using their commands
  $ns namtrace-all $trace_nam
  $ns trace-all $trace_all
Closing trace file and starting NAM
  proc finish { } {
    global ns trace_nam trace_all
    $ns flush-trace
    close $trace_nam
    close $trace_all
    exec nam out.nam &
    exit 0 }

## Slide 21: Topology Creation
Creating two nodes
    set n0 [$ns node]
    set n1 [$ns node]
Creating links (topology) between two nodes
  $ns duplex-link $n0 $n1 1Mb 10ms DropTail

## Slide 22: Attaching Agents
Create a TCP agent and attach it to node n0
set tcp0 [new Agent/TCP]
$ns attach-agent $n0 $tcp0
Create a TCP sink and attach to node 1
set sink0 [new Agent/TCPSink]
$ns attach-agent $n1 $sink0
Connect the traffic sources with the traffic sinks
$ns connect $tcp0 $sink0

## Slide 23: Traffic Generation
Create FTP application and attach it to agents
set ftp0 [new Application/FTP]
$ftp0 attach-agent $tcp0
Start and stop ftp
$ns at 0.5 "$ftp0 start"
$ns at 10.0 "$ftp0 stop"
Call the finish procedure after 10.1 seconds of simulation time
$ns at 10.1 "finish"
Run the simulation
$ns run

## Slide 24: Wired Network- TCP
0
1
TCP/FTP packet
ACK packet

## Slide 25: Wired Network- Dynamic
Network Topology

## Slide 26: Simulator Creation and Tracing Activation
Creating a Simulator Object
  set ns [new Simulator]
Tell the simulator to use dynamic routing
$ns rtproto DV
Setting up files for trace & NAM
  set trace_nam [open out.nam w]
  set trace_all [open all.tr w]
Tracing files using their commands
  $ns namtrace-all $trace_nam
  $ns trace-all $trace_all
Closing trace file and starting NAM
  proc finish { } {
    global ns trace_nam trace_all
    $ns flush-trace
    close $trace_nam $trace_all
    exec nam out.nam & exit 0 }

## Slide 27: Topology Creation
Creating seven nodes
for {set i 0} {$i < 7} {incr i} {
set n($i) [$ns node]
}
Create links between the nodes
for {set i 0} {$i < 7} {incr i} {
$ns duplex-link $n($i) $n([expr ($i+1)%7]) 1Mb 10ms DropTail
}

## Slide 28: Attaching Agents
Create a UDP agent and attach it to node n(0)
set udp0 [new Agent/UDP]
$ns attach-agent $n(0) $udp0
Create a CBR traffic source and attach it to udp0
set cbr0 [new Application/Traffic/CBR]
$cbr0 set packetSize_ 500
$cbr0 set interval_ 0.005
$cbr0 attach-agent $udp0
Create a Null agent (a traffic sink) and attach it to node n(3)
set null0 [new Agent/Null]
$ns attach-agent $n(3) $null0
Connect the traffic source with the traffic sink
$ns connect $udp0 $null0

## Slide 29: Traffic Generation
Schedule events for the CBR agent and the network dynamics
$ns at 0.5 "$cbr0 start"
$ns rtmodel-at 1.0 down $n(1) $n(2)
$ns rtmodel-at 2.0 up $n(1) $n(2)
$ns at 4.5 "$cbr0 stop“
Call the finish procedure after 5 seconds of simulation time
$ns at 5.0 "finish"
Run the simulation
$ns run

## Slide 30: Wired Network- Dynamic
Packet Drops due to link failure

## Slide 31: Wired Network- Dynamic
Dynamic Route Recovery

## Slide 32: Wired Network
Network/Traffic Topology

## Slide 33: Simulator Creation
Creating a Simulator Object
  set ns [new Simulator]
Setting up files for trace & NAM
  set trace_nam [open out.nam w]
  set trace_all [open all.tr w]
Tracing files using their commands
  $ns namtrace-all $trace_nam
  $ns trace-all $trace_all
Closing trace file and starting NAM
  proc finish { } {
    global ns trace_nam trace_all
    $ns flush-trace
    close $trace_nam
    close $trace_all
    exec nam out.nam &
    exit 0 }

## Slide 34: Topology Creation
Creating nodes
    set n1 [$ns node]
    set n2 [$ns node]
    set n3 [$ns node]
    set n4 [$ns node]
    set r1 [$ns node]
    set r2 [$ns node]
Creating links (topology)
  $ns duplex-link $n1 $r1 2Mb 5ms DropTail
  set DuplexLink0 [$ns link $n1 $r1]
  $ns duplex-link $n2 $r1 2Mb 5ms DropTail
  set DuplexLink1 [$ns link $n2 $r1]
  $ns duplex-link $r1 $r2 1Mb 10ms DropTail
  set DuplexLink2 [$ns link $r1 $r2]
  $ns duplex-link $r2 $n3 2Mb 5ms DropTail
  set DuplexLink3 [$ns link $r2 $n3]
  $ns duplex-link $r2 $n4 2Mb 5ms DropTail
  set DuplexLink4 [$ns link $r2 $n4]

## Slide 35: Topology Creation
Orientation of links
  $ns duplex-link-op $n1 $r1 orient right-down
  $ns duplex-link-op $n2 $r1 orient right-up
  $ns duplex-link-op $r1 $r2 orient right
  $ns duplex-link-op $r2 $n3 orient right-up
  $ns duplex-link-op $r2 $n4 orient right-down

## Slide 36: Attaching Agents
Attaching tcp agent to node 1
set tcp1 [new Agent/TCP]
$ns attach-agent $n1 $tcp1
Attaching sink agent to node 3
set sink1 [new Agent/TCPSink]
$ns attach-agent $n3 $sink1
Connecting tcp agent and sink agent
$ns connect $tcp1 $sink1
Attaching tcp agent to node 2
set tcp2 [new Agent/TCP]
$ns attach-agent $n2 $tcp2
Attaching sink agent to node 4
set sink2 [new Agent/TCPSink]
$ns attach-agent $n4 $sink2
Connecting tcp agent and sink agent
$ns connect $tcp2 $sink2

## Slide 37: Traffic Generation
Attaching Application (FTP)
set ftp0 [new Application/FTP]
$ftp0 attach-agent $tcp1
set ftp1 [new Application/FTP]
$ftp1 attach-agent $tcp2
Schedule events for the FTP
$ns at 0.5 "$ftp0 start“
$ns at 0.5 "$ftp1 start“
$ns at 10.1 "$ftp0 stop“
$ns at 10.2 "$ftp1 stop“
Call the finish procedure after 10.3 seconds of simulation time
$ns at 10.3 "finish“
Run the simulation
$ns run

## Slide 38: NAM Output

## Slide 39: Wireless Networks: MANETs
Scenario
  containing 2 mobile nodes
  moving within 500mX500m flat topology
  using AODV/DSR/DSDV ad hoc routing protocol
  Random Waypoint mobility model
  TCP and FTP traffic

## Slide 40: Define Variables
# ======================================================================
# Define options
# ======================================================================
set val(chan) Channel/WirelessChannel ;# channel type
set val(prop) Propagation/TwoRayGround ;# radio-propagation model
set val(netif) Phy/WirelessPhy ;# network interface type
set val(mac) Mac/802_11 ;# MAC type
set val(ifq) Queue/DropTail/PriQueue ;# interface queue type
set val(ll) LL ;# link layer type
set val(ant) Antenna/OmniAntenna ;# antenna model
set val(ifqlen) 50 ;# max packet in ifq
set val(nn) 2 ;# number of mobilenodes
set val(rp) DSDV ;# routing protocol

## Slide 41: Simulator Creation
# Create Simulator
set ns_ [new Simulator]
# Setting up files for trace & NAM
set tracefd [open simple.tr w]
set namtrace [open simple.nam w]
# Tracing files using their commands
$ns_ trace-all $tracefd
$ns_ namtrace-all-wireless $namtrace 500 500
# Closing trace file and starting NAM
proc stop {} {
global ns_ tracefd namtrace
$ns_ flush-trace
close $tracefd
close $namtrace
exec nam simple.nam & exit 0
}

## Slide 42: Create Topology
# set up topography object
set topo [new Topography] #Create topology
$topo load_flatgrid 500 500 #Create Topological Boundary (500 m X 500 m)
# Create God
create-god $val(nn)

## Slide 43: Configure Node
$ns_ node-config -adhocRouting $val(rp) \
-llType $val(ll) \
-macType $val(mac) \
-ifqType $val(ifq) \
-ifqLen $val(ifqlen) \
-antType $val(ant) \
-propType $val(prop) \
-phyType $val(netif) \
-channelType $val(chan) \
-topoInstance $topo \
-agentTrace ON \
-routerTrace ON \
-macTrace OFF \
-movementTrace OFF
for {set i 0} {$i < $val(nn) } {incr i} {
set node_($i) [$ns_ node]
$node_($i) random-motion 0 ;# disable random motion
$ns_ initial_node_pos $node_($i) 25
}

## Slide 44: Node Position and Mobility
# Provide initial (X,Y, for now Z=0) co-ordinates for mobile nodes
$node_(0) set X_ 5.0
$node_(0) set Y_ 2.0
$node_(0) set Z_ 0.0
$node_(1) set X_ 390.0
$node_(1) set Y_ 385.0
$node_(1) set Z_ 0.0
# Now produce some simple node movements
# Node_(1) starts to move towards node_(0)
$ns_ at 50.0 "$node_(1) setdest 25.0 20.0 15.0"
$ns_ at 10.0 "$node_(0) setdest 20.0 18.0 1.0"
# Node_(1) then starts to move away from node_(0)
$ns_ at 100.0 "$node_(1) setdest 490.0 480.0 15.0"

## Slide 45: Traffic Generation
# Setup traffic flow between nodes
# TCP connections between node_(0) and node_(1)
set tcp [new Agent/TCP]
$tcp set class_ 2
set sink [new Agent/TCPSink]
$ns_ attach-agent $node_(0) $tcp
$ns_ attach-agent $node_(1) $sink
$ns_ connect $tcp $sink
set ftp [new Application/FTP]
$ftp attach-agent $tcp
$ns_ at 10.0 "$ftp start"

## Slide 46: End Simulation
# Tell nodes when the simulation ends
#
for {set i 0} {$i < $val(nn) } {incr i} {
$ns_ at 150.0 "$node_($i) reset";
}
$ns_ at 150.0 "stop"
$ns_ at 150.01 "puts \"NS EXITING...\" ; $ns_ halt“
puts "Starting Simulation..."
$ns_ run

## Slide 47: Scenario Generator: Mobility
Mobile Movement Generator
  Syntax: ./setdest -n <num_of_nodes> -p <pausetime> -M <maxspeed> -t <simtime> -x <maxx> -y <maxy> > <movment-file>
  Example: ./setdest -n 20 -p 2.0 -M 10.0 -t 200 -x 500 -y 500 > scen-20-test
  Source Directory: ns-2/indep-utils/cmu-scen-gen/setdest/
  Inclusion in TCL script: source <movement-file>
Random movement
  $node random-motion 1
  $node start

## Slide 48: A Movement Scenario: scen-20-test
$node_(2) set Z_ 0.000000000000
$node_(2) set Y_ 199.373306816804
$node_(2) set X_ 591.256560093833
$node_(1) set Z_ 0.000000000000
$node_(1) set Y_ 345.357731779204
$node_(1) set X_ 257.046298323157
$node_(0) set Z_ 0.000000000000
$node_(0) set Y_ 239.438009831261
$node_(0) set X_ 83.364418416244
$ns_ at 50.000000000000 "$node_(2) setdest 369.463244915743 170.519203111152 3.371785899154"
$ns_ at 51.000000000000 "$node_(1) setdest 221.826585497093 80.855495003839 14.909259208114"
$ns_ at 33.000000000000 "$node_(0) setdest 89.663708107313 283.494644426442 19.153832288917"

## Slide 49: Scenario Generator: Traffic
Generating traffic pattern files
  CBR/TCP traffic
  ns cbrgen.tcl [-type cbr|tcp] [-nn nodes] [-seed seed] [-mc connections] [-rate rate] > [file-name]
  CBR traffic
  ns cbrgen.tcl –type cbr –nn 20 –seed 1 –mc 8 - rate 4 > cbr-20-test
  TCP traffic
  ns cbrgen.tcl –type tcp -nn 15 -seed 0 –mc 6 > tcp-15-test
Source Directory: ns-2/indep-utils/cmu-scen-gen/
Inclusion in TCL file:
source <traffic-scenario-file>

## Slide 50: A Traffic Scenario: cbr-20-test
set udp_(0) [new Agent/UDP]
$ns_ attach-agent $node_(0) $udp_(0)
set null_(0) [new Agent/Null]
$ns_ attach-agent $node_(2) $null_(0)
set cbr_(0) [new Application/Traffic/CBR]
$cbr_(0) set packetSize_ 512
$cbr_(0) set interval_ 4.0
$cbr_(0) set random_ 1
$cbr_(0) set maxpkts_ 10000
$cbr_(0) attach-agent $udp_(0)
$ns_ connect $udp_(0) $null_(0)
$ns_ at 127.93667922166023 "$cbr_(0) start"
…….

## Slide 51: Energy Extension
Node is energy-aware
Define node by adding new options:
$ns_ node-config \
–energyModel EnergyModel
    -initialEnergy 100.0
    -txPower 0.6
    -rxPower 0.2

## Slide 52: Further Reading
Jae Chung and Mark Claypool, NS by Example, http://nile.wpi.edu/NS/
The ns manual, http://www.isi.edu/nsnam/ns/ns-documentation.html
Marc Greis' Tutorial for the Network Simulator ns, http://www.isi.edu/nsnam/ns/tutorial/